## Slide 1: CSE 205: Digital Logic Design
Dr. Tanzima Hashem
Associate Professor
CSE, BUET

## Slide 2: Sequential Circuits
Consist of a combinational circuit to which storage elements are connected to form a feedback path
Specified by a time sequence of inputs, outputs and internal states

## Slide 3: Synchronous Sequential Circuit
Synchronous sequential circuits
  Synchronized by a periodic train of clock pulses
  Much easier to design (preferred design style)

## Slide 4: Asynchronous Sequential Circuit
Inputs / Outputs
Delay elements:
  Only a short term memory
  May not really exist due to original gate delay
Secondary variable:
  Current state (small y)
Excitation variable:
  Next state (big Y)
  Have some delay in response to input changes
Block diagram of an asynchronous sequential circuit

## Slide 5: Asynchronous Sequential Circuit
Internal states can change at any instant of time when there is a change in the input variables
No clock signal is required
Have better performance but hard to design due to timing problems
Block diagram of an asynchronous sequential circuit

## Slide 6: Why Asynchronous Circuits?
Used when speed of operation is important
  Response quickly without waiting for a clock pulse
Used in small independent systems
  Only a few components are required
Used when the input signals may change independently of internal clock
  Asynchronous in nature
Used in the communication between two units that have their own independent clocks
  Must be done in an asynchronous fashion

## Slide 7: Operational Mode
Steady-state condition:
  Current states and next states are the same
  Difference between Y and y will cause a transition
Fundamental mode:
  No simultaneous changes of two or more variables
  The time between two input changes must be longer than the time it takes the circuit to a stable state
  The input signals change one at a time and only when the circuit is in a stable condition

## Slide 8: Analysis Procedure Transition Table
Transition table is useful to analyze an asynchronous circuit from the circuit diagram
Procedure to obtain transition table:
  1. Determine all feedback loops in the circuits
  2. Mark the input (yi) and output (Yi) of each feedback loop
  3. Derive the Boolean functions of all Y’s
  4. Plot each Y function in a map and combine all maps into one table
  5. Circle those values of Y in each square that are equal to the value of y in the same row

## Slide 9: An Example of Transition Table
  The excitation variables: Y1 and Y2
  Y1 = xy1+ x'y2
  Y2 = xy1' + x'y2
Fig. 9.2
Example of an asynchronous sequential circuit

## Slide 10: An Example of Transition Table
  Maps and transition table
y variables for the rows
External variable for the columns
Circle the stable states
  Y = y
Fig. 9.3
Maps and transition table for the circuit of Fig. 9.2

## Slide 11: State Table
When input x changes from 0 to 1 while y=00:
  Y changes to 01  unstable
  y becomes 01 after a short delay  stable at the second row

## Slide 12: Flow Table
Similar to a transition table except the states are represented by letter symbols
Can also include the output values
Suitable to obtain the logic diagram from it
Primitive flow table:
  only one stable state in each row
Equivalent to 9-3(c) if
a=00, b=01, c=11, d=10
Fig. 9.4
Example of flow tables

## Slide 13: Flow Table to Circuits
Procedure to obtain circuits from flow table:
  Assign to each state a distinct binary value (convert to a transition table)
  Obtain circuits from the map
Two difficulties:
  The binary state assignment (to avoid race)
  The output assigned to the unstable states

## Slide 14: Flow Table to Circuits
Fig. 9.5
Derivation of a circuit specified by the flow table of Fig. 9.4(b)

## Slide 15: Race Conditions
Race condition:
  two or more binary state variables will change value when one input variable changes
  Cannot predict state sequence if unequal delay is encountered
  00 ® 11
    00 ® 10 ® 11 or 00 ® 01 ® 11
Non-critical race:
  The final stable state does not depend on the change order of state variables
Critical race:
  The change order of state variables will result in different stable states
  Should be avoided !!

## Slide 16: Noncritical Race: Examples

## Slide 17: Critical Race: Examples

## Slide 18: Race Conditions
Race can be avoided by proper state assignment
  Direct the circuit through intermediate unstable states with a unique state-variable change
  It is said to have a cycle
Must ensure that a cycle will terminate with a stable state
  Otherwise, the circuit will keep going in unstable states

## Slide 19: Cycles
Fig: Examples of cycles
A cycle
    a unique sequence of unstable states

## Slide 20: Stability Check
Asynchronous sequential circuits may oscillate between unstable states due to the feedback
  Must check for stability to ensure proper operations
Can be easily checked from the transition table
  Any column has no stable states  unstable

## Slide 21: Example of an Unstable Circuit
Fig. 9.9: Example of an unstable circuit
When x1x2=11 in Fig. 9-9(b), Y and y are never the same
a square waveform generator?

## Slide 22: Circuits with Latches
The traditional configuration of asynchronous circuits is using one or more feedback loops
  No real delay elements
It is more convenient to employ the SR latch as a memory element in asynchronous circuits
  Produce an orderly pattern in the logic diagram with the memory elements clearly visible
SR latch is also an asynchronous circuit
  Will be analyzed first using the method for asynchronous circuits

## Slide 23: SR Latch with NOR Gates
Fig. 9.10: SR latch with NOR gates

## Slide 24: SR Latch with NOR Gates
Y = ((S+y)'+R)' = (S+y)R' = SR'+R'y
An unpredictable result when SR: 11 ® 00
SR = 0 in operation
Y = S + R'y when SR = 0

## Slide 25: SR Latch with NAND Gates
Fig. 9.11: SR latch with NAND gates

## Slide 26: SR Latch with NAND Gates
Two cross-coupled NAND gate
  S'R' = 0
  Y = (S(Ry)')' = S'+ Ry
  S'R' latch

## Slide 27: Analysis Procedure
Procedure to analyze an asynchronous sequential circuits with SR latches:
  1. Label each latch output with Yi and its external feedback path (if any) with yi
  2. Derive the Boolean functions for each Si and Ri
  3. Check whether SR=0 (NOR latch) or S’R’=0 (NAND latch) is satisfied
  4. Evaluate Y=S+R’y (NOR latch) or Y=S’+Ry(NAND latch)
  5. Construct the transition table for Y=Y1Y2…Yk
  6. Circle all stable states where Y=y

## Slide 28: Analysis Example
Fig. 9.12: Examples of a circuit with SR latch

## Slide 29: Analysis Example
Label each latch output with Yi and its external feedback path with yi
Derive the Boolean functions for the Si and Ri
  S1 = x1y2
  R1 = x'1x'2
  S2 = x1x2
  R2 = x'2y1
Check whether SR=0 for each NOR latch or whether S'R'=0 for each NAND latch
  S1R1 = x1y2x'1x'2 = 0
  S2R2 = x1x2x'2y1 = 0

## Slide 30: Analysis Example
Evaluate Y = S +R'y for each NOR latch or Y = S' + Ry for each NAND latch
  Y1 = x1y2 + (x1+x2)y1 = x1y2+x1y1+x2y1
  Y2 = x1x2 + (x2+y'1)y2 = x1x2+x2y2+y'1y2
Construct the state transition table
Circle all stable states

## Slide 31: Analysis Example
Race example:
  Let initial state is
  y1y2x1x2=1101
  input x2 is changed to 0
  if Y1 change to 0 before Y2
  then y1y2x1x2=0100
  instead of 0000
Fig. 9.13
Transition table for the circuit of Fig. 9.

## Slide 32: Latch Excitation Table
For SR latch:
0

## Slide 33: Implementation Procedure
Procedure to implement an asynchronous sequential circuits with SR latches:
  1. Given a transition table that specifies the excitation function Y = Y1Y2…Yk, derive a pair of maps for each Si and Ri using the latch excitation table
  2. Derive the Boolean functions for each Si and Ri (do not to make Si and Ri equal to 1 in the same minterm square)
  3. Draw the logic diagram using k latches together with the gates required to generate the S and R (for NAND latch, use the complemented values in step 2)

## Slide 34: Implementation Example
Determine the Boolean functions for the S and R inputs of each latch
Given a transition table
From maps: the simplified Boolean functions are
NOR latch
NAND latch

## Slide 35
Fig. 9.14
Derivation of a latch circuit from a transition table

## Slide 36: Debounce Circuit
Mechanical switches are often used to generate binary signals to a digital circuit
  It may vibrate or bounce several times before going to a final rest
  Cause the signal to oscillate between 1 and 0

## Slide 37: Debounce Circuit
A debounce circuit can remove the series of pulses from a contact bounce and produce a single smooth transition
  Position A (SR=01)  bouncing (SR=11) Position B (SR=10)
  Q = 1 (set)  Q = 1 (no change)  Q = 0 (reset)
Fig. 9.15: Debounce circuit

## Slide 38: Design Procedure
Design specifications
(i) Obtain a primitive table from specifications
(ii) Reduce flow table by merging rows in the primitive flow table
(iii) Assign binary state variables to each row of reduced table
(iv) Assign output values to dashes associated with unstable states to obtain the output map
(v) Simplify Boolean functions for excitation and output variables;
(vi) Draw the logic diagram

## Slide 39: Design Procedure: Example
Design specifications
  a gated latch
  two inputs, G (gate) and D (data)
  one output, Q
  G = 1: Q follows D
  G = 0 : Q remains unchanged
Assume fundamental mode operation – only one input changes at a time.

## Slide 40: Design Procedure: Example
Form a table with all possible total states

## Slide 41: Primitive Flow Table
Obtain the flow table by listing all possible states
  Dash marks are given when both inputs change simultaneously
  Outputs of unstable states are don’t care
Fig. 9.16
Primitive flow table

## Slide 42: Reduce the Flow Table
Reduction of the primitive flow table
  two or more rows in the primitive flow table can be merged if there are non-conflicting states and outputs in each of the columns

## Slide 43: Reduce the Flow Table
Fig. 9.17: Reduction of the primitive flow table

## Slide 44: Transition Table and Output Map
Fig. 9.18: Transition table and output map for gated latch
Assign a binary value to each state to generate the transition table
  a=0, b=1 in this example

## Slide 45: Logic Diagram
Directly use the simplified Boolean function for the excitation variable Y
  An asynchronous circuit without latch is produced
Fig. 9.19
Gated-latch logic diagram

## Slide 46: Design with SR Latches
We can also implement asynchronous circuits using latches at the outputs.
Given the map for each excitation variable Y, derive necessary equations for S and R of a latch to produce Y.
Derive Boolean equations for S and R.

## Slide 47: Design with SR Latches
Fig. 9.20
Circuit with SR latch

## Slide 48: Outputs for Unstable States
Objective: no momentary false outputs occur when the circuit switches between stable states
If the output value is not changed, the intermediate unstable state must have the same output value
  0  1 (unstable)  0 (X)
If the output value changed, the intermediate outputs are don’t care
It makes no difference when the output change occurs

## Slide 49: Design Procedure
Summary
  a primitive flow table
  state reduction
  state assignment
  output assignment
  Simplify the Boolean functions of the excitation and output variables and draw the logic diagram

## Slide 50: Reduction of State and Flow Table
State reduction procedure is similar in both sync. & async. sequential circuits
For completely specified state tables:
  use implication table
For incompletely specified state tables:
  use compatible pairs states

## Slide 51: Reduction of State and Flow Table
Two states are equivalent if they have the same output and go to the same (equivalent) next states for each possible input
Example:
  (a,b) are equivalent if (c,d) are equivalent
  (a,b) imply (c,d)
  (c,d) imply (a,b)

## Slide 52: State Reduction:Implication Table

## Slide 53: State Reduction: Implication Table
  Finally, all the squares that have no crosses are recorded with check marks. The equivalent states are: (a, b), (d, e), (d, g), (e, g).
  We now combine pairs of states into larger groups of equivalent states. The last three pairs can be combined into a set of three equivalent states (d, e, g) because each one of the states in the group is equivalent to the other two.

## Slide 54: State Reduction: Implication Table
  The final partition of these states consists of the equivalent states found from the implication table, together with all the remaining states in the state table that are not equivalent to any other state: (a, b) (c) (d, e, g) (f)

## Slide 55: Merging of the Flow Table
The state table may be incompletely specified
  Some next states and outputs are don’t care
Primitive flow tables are always incompletely specified
  Several synchronous circuits also have this property
Incompletely specified states are not “equivalent”
  Instead, we are going to find “compatible” states
  Two states are compatible if they have the same output and compatible next states whenever specified
Three procedural steps:
  Determine all compatible pairs
  Find the maximal compatibles
  Find a minimal closed collection of compatibles

## Slide 56: Compatible Pairs
Compatible pairs
    (a,b) (a,c) (a,d) (b,e) (b,f) (c,d) (e,f)

## Slide 57: Maximal Compatibles
A group of compatibles that contains all the possible combinations of compatible states
  Obtained from a merger diagram
  A line in the diagram represents that two states are compatible
n-state compatible  n-sided fully connected polygon
  All its diagonals connected
Not all maximal compatibles are necessary

## Slide 58: Maximal Compatibles
Fig. 9.24
Merger diagram
  an isolated dot: a state that is not compatible to any other state
  a line: a compatible pair
  a triangle: a compatible with three states
  an n-state compatible: an n-sided polygon with all its diagonals connected

## Slide 59: Closed Covering Condition
The set of chosen compatibles must cover all the states and must be closed
The closure condition is satisfied if
  no implied states or the implied states are included within the set
Ex: if remove (a,b) in the right
  (a,c,d) (b,e,f) are left in the set
  All six states are still included
  No implied states according to
  its implication table

## Slide 60: Closed Covering Condition
*(a,b) (c,d,e)  (X)
implied (b,c) is not
included in the set
*better choice:
(a,d) (b,c) (c,d,e)
all implied states
are included

## Slide 61: Race-Free State Assignment
Objective: choose a proper binary state assignment to prevent critical races
Only one variable can change at any given time when a state transition occurs
States between which transitions occur will be given adjacent assignments
  Two binary values are said to be adjacent if they differ in only one variable
To ensure that a transition table has no critical races, every possible state transition should be checked
  A tedious work when the flow table is large
  Only 3-row and 4-row examples are demonstrated

## Slide 62: 3-Row Flow Table Example
Three states require two binary variables
Outputs are omitted for simplicity
Adjacent info. are represented by a transition diagram
a and c are still not adjacent in such an assignment!!
  Impossible to make all states adjacent if only 3 states are used

## Slide 63: 3-Row Flow Table Example
A race-free assignment can be obtained if we add an extra row to the flow table
  Only provide a race-free transition between the stable states
The transition from a to c must now go through d
  00  10  11 (no race condition)

## Slide 64: 4-Row Flow Table Example
Sometimes, just one extra row may not be sufficient to prevent critical races
  More binary state variables may also required
With one or two diagonal transitions, there is no way of using two binary variables that satisfy all adjacency

## Slide 65: 4-Row Flow Table Example

## Slide 66: Multiple-Row Method
Multiple-row method is easier
  May not as efficient as in above shared-row method
Each stable state is duplicated with exactly the same output
  Behaviours are still the same
While choosing the next states, choose the adjacent one

## Slide 67: Hazards
Unwanted switching appears at the output of a circuit
  Due to different propagation delay in different paths
May cause the circuit to mal-function
  Cause temporary false-output values in combinational circuits
  Cause a transition to a wrong state in asynchronous circuits
  Not a concern to synchronous sequential circuits

## Slide 68: Hazards in Combinational Circuits
Fig. 9.33
Circuits with hazards

## Slide 69: Types of Hazards
Three types of hazards:
Fig. 9.34
Types of hazards

## Slide 70: Hazard Free Circuit
Static 1-hazard (sum of products)
    the removal of static 1-hazard guarantees that no static 0-hazards or dynamic hazards
Static 0-hazard (product of sum)
    Y = (x1+x2')(x2+x3)
The remedy
  the circuit moves from one product term to another
  additional redundant gate

## Slide 71: Hazard Free Circuit

## Slide 72: Hazard in a Asynchronous Circuit
Fig. 9.37
Hazard in a asynchronous sequential circuit
  In general, no problem for synchronous design

## Slide 73: Remove Hazard with Latches
Implement the asynchronous circuit with SR latches can also remove static hazards
  A momentary 0 has no effects to the S and R inputs of a NOR latch
  A momentary 1 has no effects to the S and R inputs of a NAND latch
Replace
by a latch

## Slide 74: Implementation with SR latches
Given:
  S = AB + CD
  R = A’C
For NAND latch, use complemented inputs
  S’ = (AB + CD)’= (AB)’(CD)’
  R’ = (A’C)’
Q = (Q’S)’ = [Q’(AB)’(CD)’]’
Two-level circuits (this is the output we want)

## Slide 75: Implementation with SR latches

## Slide 76: Essential Hazards
Besides static and dynamic hazards, another type of hazard in asynchronous circuits is called essential hazard
Caused by unequal delays along two or more paths that originate from the same input
Cannot be corrected by adding redundant gates
Can only be corrected by adjusting the amount of delay in the affected path
  Each feedback path should be examined carefully !!

## Slide 77: Summary of Design Procedure
1. State the design specifications
2. Derive a primitive flow table
3. Reduce the flow table by merging the rows
4. Make a race-free binary state assignment
5. Obtain the transition table and output map
6. Obtain the logic diagram using SR latches

## Slide 78: Design Specification
Design a negative-edge-triggered T flip-flop
  Two inputs: T(toggle) and C(clock)
  T=1: toggle, T=0: no change
  One output: Q

## Slide 79: Primitive Flow Table

## Slide 80: Merging of the Flow Table
Compatible pairs:
Maximal compatible set:

## Slide 81: State Assignment and Transition Table
No diagonal lines in the transition diagram
  No need to add extra states

## Slide 82: Logic Diagram

## Slide 83: Syllabus
Chapter 9