## Slide 1: CSE 205: Digital Logic Design

## Slide 2: Logic Minimization
The complexity of the digital logic gates
  The complexity of the algebraic expression
Algebraic approaches:
  The procedure of simplifying Boolean expressions is difficult since it lacks specific rules to predict the successive steps in the simplification process.

## Slide 3: The Map Method
The Karnaugh map (K-Map)
    A simple straight forward procedure
    A pictorial form of a truth table
A diagram made up of squares
  Each square represents one minterm

## Slide 4: Two-Variable Map
Four minterms
A' = row 0; A = row 1
B' = column 0; B = column 1

## Slide 5: Example

## Slide 6: Example

## Slide 7: Three-Variable Map
Eight minterms
The Gray code sequence
Any two adjacent squares in the map differ by only on variable

## Slide 8: Three-Variable Map
m0 and m2 (m4 and m6) are adjacent
m0+ m2 = A'B'C' + A'BC' = A'C' (B'+ B) = A'C'
m4+ m6 = AB'C' + A'BC' = AC' (B'+ B) = AC'

## Slide 9: Example

## Slide 10: Example
Simplify the Boolean function F(x, y, z)= S(2, 3, 4, 5)
  F(x, y, z) = S(2, 3, 4, 5) = x'y + xy'

## Slide 11: Example
Simplify F(x, y, z) = S(3, 4, 6, 7)
  F(x, y, z) = S(3, 4, 6, 7) = yz+ xz'

## Slide 12: Four adjacent Squares
Consider four adjacent squares
  m0+m2+m4+m6 = x'y'z'+x'yz'+xy'z'+xyz' = x'z'(y'+y) +xz'(y'+y) = x'z' + xz‘ = z'
  m1+m3+m5+m7 = x'y'z+x'yz+xy'z+xyz =x'z(y'+y) + xz(y'+y) =x'z + xz = z

## Slide 13: Example
Simplify F(x, y, z) = S(0, 2, 4, 5, 6)
  F(x, y, z) = S(0, 2, 4, 5, 6) = z'+ xy'

## Slide 14: Example
Let F = A'C + A'B + AB'C + BC
  Express it in sum of minterms.
  Find the minimal sum of products expression.
  F(A, B, C) = S(1, 2, 3, 5, 7) = C + A'B

## Slide 15: Four-Variable Map
16 minterms
Combinations of 2, 4, 8, and 16 adjacent squares

## Slide 16: Example 3.5
Example 3.5: simplify F(w, x, y, z) = S(0, 1, 2, 4, 5, 6, 8, 9, 12, 13, 14)
  F = y'+w'z'+xz'

## Slide 17: Example
Simplify F = ABC + BCD + ABCD + ABC
ABC + BCD + ABCD + ABC= BD + BC +ACD

## Slide 18: Prime Implicants
All the minterms are covered.
Minimize the number of terms.
There are no redundant terms.
Implicant: A group of one or more k map cell
Prime implicant: an implicant that is not a subset of another implicant
Essential Prime Implicant: a prime implicant that covers at least one cell not covered by another prime implicant

## Slide 19: Prime Implicants
F(A, B, C, D) = Σ(0, 2, 3, 5, 7, 8, 9, 10, 11, 13, 15)
  The simplified expression may not be unique
  F = BD+B'D'+CD+AD = BD+B'D'+CD+AB'
  = BD+B'D'+B'C+AD = BD+B'D'+B'C+AB'

## Slide 20: Five-Variable Map
Map for more than four variables becomes complicated
  Five-variable map: two four-variable map (one on the top of the other).

## Slide 21: Example
Simplify F = S(0, 2, 4, 6, 9, 13, 21, 23, 25, 29, 31)
F = A'B'E'+BD'E+ACE

## Slide 22: Example
Another Map for F = A'B'E'+BD'E+ACE

## Slide 23: Six-Variable Map
Another Map for F = A'B'E'+BD'E+ACE

## Slide 24: Don't-Care Conditions
The value of a function is not specified for certain combinations of variables
  BCD; 1010-1111
The unspecified minterms of a function are called the don’t-care conditions, or simply the don’t-cares, and are denoted as Xs.
These don’t-care conditions can be used on a map to provide further simplification of the Boolean expression.
  Can be implemented as 0 or 1

## Slide 25: Example
Simplify F(w, x, y, z) = S(1, 3, 7, 11, 15) which has the don't-care conditions d(w, x, y, z) = S(0, 2, 5).
F = yz + w'x'; F = yz + w'z
F = S(0, 1, 2, 3, 7, 11, 15) ; F = S(1, 3, 5, 7, 11, 15)

## Slide 26: Don't-Care Conditions
Either one of the above expressions satisfies the conditions stated.
Note that the above 2 expressions represent 2 functions that are algebraically unequal: each covers different don’t-care terms.
We may or may not include any of the Xs, while all the 1s must be included.

## Slide 27: Product of Sums Simplification
Simplify F' in the form of sum of products
Apply DeMorgan's theorem F = (F')'
F': sum of products → F: product of sums

## Slide 28: Example
Simplify F = S(0, 1, 2, 5, 8, 9, 10) into (a) sum-of-products form, and (b) product-of-sums form:
  F(A, B, C, D)= S(0, 1, 2, 5, 8, 9, 10) = B'D'+B'C'+A'C'D
  F' = AB+CD+BD'
    Apply DeMorgan's theorem; F=(A'+B')(C'+D')(B'+D)

## Slide 29: Example (cont.)
Gate implementation of F = S(0, 1, 2, 5, 8, 9, 10)
Figure 3.15 Gate Implementation of F = S(0, 1, 2, 5, 8, 9, 10)
Product-of sums form
Sum-of products form

## Slide 30: Product of Maxterms
Consider the function defined in Table 3.2.
  In sum-of-minterm:
  In sum-of-maxterm:

## Slide 31: Product of Maxterms
Consider the function defined in Table 3.2.
  Combine the 1’s:
  Combine the 0’s :
  Taking the complement of F'
Figure 3.16 Map for the function of Table 3.2
'

## Slide 32: Map Method: Summary
Simplification procedure:
  Generate K-map.
  Determine PIs.
  Select EPIs.
  Find minimal cover (set) of PIs.

## Slide 33: Simplification of Boolean functions
3 common methods:
Boolean algebra
  The basis for all methods
  Difficult to see the best path to take and to know when you are finished
Karnaugh maps
  Fast and easy for 2 – 6 variables
  Pictorial approach based on recognition of patterns
  Difficult for large numbers of variables
Tabulation methods
  Tedious to perform by hand, but well suited to computer implementation
  No limit on the number of variables

## Slide 34: Tabulation Methods
The tabulation method was first formulated by Quine and later improved by McCluskey. It is also known as the Quine-McCluskey method.
Simplification consists of two parts:
  To find candidate prime implicants.
  To choose the prime implicants that give an expression with the least number of literals (i.e., minimal cover generation).

## Slide 35: Determination of prime implicants
Group minterms by number of 1s.
Compare minterms and find pairs with distance 1.
Generate subcubes.
Repeat the above procedure on generated subcubes until no more subcubes can be generated.

## Slide 36: Determination of prime implicants
F(w,x,y,z) = ∑(0, 1, 2, 8, 10, 11, 14, 15)
= w'x'y' + x'z' + wy

## Slide 37: Determination of prime implicants
Step 1: Group the minterms according to the number of 1s (see Column (a)).
Step 2: Combine any 2 minterms that differ from each other by exactly one variable (i.e., dist-1), the unmatched variable removed (see Column (b)). Try this for all possible pairs of minterms. A check (3) is placed to the right of both minterms if they have been used in a match.

## Slide 38: Determination of prime implicants
Step 3: Repeat the process. Combine any 2 product terms from Step ­ that differ from each other by exactly one variable, the unmatched variable removed (see Column (c)).
Step 4: The unchecked terms in the table form the PIs. Some of the product terms may appear twice in the table. It of course is unnecessary to use the same term twice.

## Slide 39: Minimal cover generation
The selection of PIs that form the minimized function is made from a PI table
F(w,x,y,z) = ∑(1, 4, 6, 7, 8, 9, 10, 11,15)

## Slide 40: Minimal cover generation
F(w,x,y,z) = ∑(1, 4, 6, 7, 8, 9, 10, 11,15)
Essential Prime implicants are x’y’z, w’xz’, wx’
F(w,x,y,z) = x’y’z + w’xz’ + wx’ + xyz
PI | Minterms | 7 | 15
w’xy | 6, 7 | X | 
xyz | 7, 15 | X | X
wyz | 11, 15 |  | X

## Slide 41: Minimal cover generation
Step 1: Check the PIs that cover minterms with a single X in their columns. These PIs are the EPIs.
Step 2: Check each column whose minterm is covered by the selected EPIs.
Step 3: If there are minterms left uncovered (7 & 15 in this example), some nonessential PIs have to be selected to cover them. We of course will select the PIs with a smallest total number of literals (xyz in this example).

## Slide 42: NAND and NOR Implementation
NAND gate is a universal gate
  Can implement any digital system
Logic Operations with NAND Gates

## Slide 43: NAND Gate
Two graphic symbols for a NAND gate
Two Graphic Symbols for NAND Gate

## Slide 44: Two-level Implementation
Two-level logic
  NAND-NAND = sum of products
  Example: F = AB+CD
  F = ((AB)' (CD)' )' =AB+CD

## Slide 45: Example

## Slide 46: Two -Level NAND Circuits
The procedure
  Simplify the function and express it in SOP form
  Draw a NAND gate for each product term
  Draw a single gate using AND-invert or invert-OR symbol for the sum term
  A term with single literal, complement if needed

## Slide 47: Multilevel NAND Circuits
The procedure
  Convert all AND gates to NAND gates
  Convert all OR gates to NAND gates with invert-OR symbols
  Balance all bubbles, insert an inverter if needed

## Slide 48: Multilevel NAND Circuits
F = A(CD + B) + BC

## Slide 49: Multilevel NAND Circuits
F = (AB +AB)(C+ D)

## Slide 50: NOR Implementation
NOR function is the dual of NAND function.
The NOR gate is also universal.
Logic Operation with NOR Gates

## Slide 51: NOR Gate
Two graphic symbols for a NOR gate
Two Graphic Symbols for NOR Gate

## Slide 52: NOR Implementation
F = (A + B)(C + D)E

## Slide 53: NOR Implementation
F = (AB +AB)(C + D)

## Slide 54: Other Two-level Implementations
Wired logic
  In some technologies, it is possible to short O/Ps of some logic gates
AND-OR-INVERT function
OR-AND-INVERT function
Wired Logic

## Slide 55: Non-degenerate Forms
16 possible combinations of two-level forms
Eight of them: degenerate forms = a single operation
  AND-AND, AND-NAND, OR-OR, OR-NOR, NAND-OR, NAND-NOR, NOR-AND, NOR-NAND.
The eight non-degenerate forms
  AND-OR, OR-AND, NAND-NAND, NOR-NOR, NOR-OR, NAND-AND, OR-NAND, AND-NOR.
  AND-OR and NAND-NAND = sum of products.
  OR-AND and NOR-NOR = product of sums.
  NOR-OR, NAND-AND, OR-NAND, AND-NOR = ?

## Slide 56: AND-OR-Invert Implementation
AND-OR-INVERT (AOI) Implementation
  NAND-AND = AND-NOR = AOI
  F = (AB+CD+E)'
  F' = AB+CD+E (sum of products)
AND-OR-INVERT circuits, F = (AB +CD +E)

## Slide 57: OR-AND-Invert Implementation
OR-AND-INVERT (OAI) Implementation
  OR-NAND = NOR-OR = OAI
  F = ((A+B)(C+D)E)'
  F' = (A+B)(C+D)E (product of sums)
  OR-AND-INVERT circuits, F = ((A+B)(C+D)E)'

## Slide 58: Tabular Summary and Examples

## Slide 59
  Other Two-level Implementations
Example

## Slide 60: Exclusive-OR Function
Exclusive-OR (XOR)
  xÅy = xy'+x'y
Exclusive-NOR (XNOR)
  (xÅy)' = xy + x'y'
Some identities
  xÅ0 = x
  xÅ1 = x'
  xÅx = 0
  xÅx' = 1
  xÅy' = (xÅy)'
  x'Åy = (xÅy)'
Commutative and associative
  AÅB = BÅA
  (AÅB) ÅC = AÅ (BÅC) = AÅBÅC

## Slide 61: Exclusive-OR Implementations
Implementations
  (x'+y')x + (x'+y')y = xy'+x'y = xÅy
Exclusive-OR Implementations

## Slide 62: Odd Function
AÅBÅC = (AB'+A'B)C' +(AB+A'B')C = AB'C'+A'BC'+ABC+A'B'C = S(1, 2, 4, 7)
XOR is a odd function → an odd number of 1's, then F = 1.
  XNOR is a even function → an even number of 1's, then F = 1.
Map for a Three-variable Exclusive-OR Function

## Slide 63: XOR and XNOR
Logic diagram of odd and even functions
Logic Diagram of Odd and Even Functions

## Slide 64: Four-variable Exclusive-OR function
Four-variable Exclusive-OR function
  AÅBÅCÅD = (AB'+A'B)Å(CD'+C'D) = (AB'+A'B)(CD+C'D')+(AB+A'B')(CD'+C'D)
Map for a Four-variable Exclusive-OR Function

## Slide 65: Parity Generation and Checking
Parity Generation and Checking
  A parity bit: P = xÅyÅz
  Parity check: C = xÅyÅzÅP
    C=1: one bit error or an odd number of data bit error
    C=0: correct or an even # of data bit error
Logic Diagram of a Parity Generator and Checker

## Slide 66: Parity Generation and Checking

## Slide 67: Parity Generation and Checking