## Slide 1: CSE 205: Digital Logic Design
Dr. Tanzima Hashem
Associate Professor
CSE, BUET

## Slide 2: Textbook
Digital Design (5th Edition)
  M. Morris Mano
  Michael D. Ciletti

## Slide 3: Combinational Logic
Combinational Logic:
  Output depends only on current input
  Has no memory

## Slide 4: Sequential Logic
Sequential Logic:
  Output depends not only on current input but also on past input values, e.g., design a counter
  Need some type of memory to remember the past input values

## Slide 5: Alarm control system
Suppose we wish to construct an alarm circuit such that the output remains active (on) even after the sensor output that triggered the alarm goes off
The circuit requires a memory element to remember that the alarm has to be active until a reset signal arrives

## Slide 6: Sequential Circuits
Consist of a combinational circuit to which storage elements are connected to form a feedback path
State:  the state of the memory devices now, also called current state
Next states and outputs are functions of inputs and present states of storage elements

## Slide 7: Two Types of Sequential Circuits
Synchronous sequential circuit
  circuit output changes only at some discrete instants of time.
  Synchronized by a periodic train of clock pulses
  Much easier to design (preferred design style)
Asynchronous sequential circuit
  circuit output can change at any time (clockless)
  May have better performance but hard to design

## Slide 8
Synchronous Sequential Circuits

## Slide 9: Memory elements
A digital circuit that can maintain a binary state indefinitely, until directed by an input signal to switch states
Differences among different types of storage elements depends on
  The number of inputs they possess
  The manner in which the inputs affect the binary state

## Slide 10: Memory elements
Latch - a level-sensitive memory element
  SR latches
  D latches
Flip-Flop - an edge-triggered memory element
  Master-slave flip-flop
  Edge-triggered flip-flop
RAM and ROM  a mass memory element

## Slide 11: Latches
A latch is binary storage element
Can store a 0 or 1
The most basic memory
Easy to build
Built with gates (NORs, NANDs, NOT)

## Slide 12: Latches
S R Q0 | Q | Q’
0 0 0 |  | 
0
1
0
0
0 | 1
Q = Q0
Initial Value
SR Latch

## Slide 13: Latches
S R Q0 | Q | Q’
0 0 0 | 0 | 1
0 0 1 |  | 
1
0
0
0
1 | 0
Q = Q0
Q = Q0
SR Latch

## Slide 14: Latches
S R Q0 | Q | Q’
0 0 0 | 0 | 1
0 0 1 | 1 | 0
0 1 0 | 0 | 
0
1
1
0
 | 1
Q = 0
Q = Q0
SR Latch

## Slide 15: Latches
S R Q0 | Q | Q’
0 0 0 | 0 | 1
0 0 1 | 1 | 0
0 1 0 | 0 | 1
0 1 1 |  | 
1
0
1
0
0 | 1
Q = 0
Q = Q0
Q = 0
SR Latch

## Slide 16: Latches
S R Q0 | Q | Q’
0 0 0 | 0 | 1
0 0 1 | 1 | 0
0 1 0 | 0 | 1
0 1 1 | 0 | 1
1 0 0 |  | 
0
1
0
1
1 | 0
Q = 0
Q = Q0
Q = 1
SR Latch

## Slide 17: Latches
S R Q0 | Q | Q’
0 0 0 | 0 | 1
0 0 1 | 1 | 0
0 1 0 | 0 | 1
0 1 1 | 0 | 1
1 0 0 | 1 | 0
1 0 1 |  | 
1
0
0
1
1 | 0
Q = 0
Q = Q0
Q = 1
Q = 1
SR Latch

## Slide 18: Latches
S R Q0 | Q | Q’
0 0 0 | 0 | 1
0 0 1 | 1 | 0
0 1 0 | 0 | 1
0 1 1 | 0 | 1
1 0 0 | 1 | 0
1 0 1 | 1 | 0
1 1 0 |  | 
0
1
1
1
0 | 0
Q = 0
Q = Q0
Q = 1
Q = Q’
0
SR Latch

## Slide 19: Latches
S R Q0 | Q | Q’
0 0 0 | 0 | 1
0 0 1 | 1 | 0
0 1 0 | 0 | 1
0 1 1 | 0 | 1
1 0 0 | 1 | 0
1 0 1 | 1 | 0
1 1 0 | 0 | 0
1 1 1 |  | 
1
0
1
1
0 | 0
Q = 0
Q = Q0
Q = 1
Q = Q’
0
Q = Q’
SR Latch

## Slide 20: SR Latch
S R | Q
0 0 | Q0
0 1 | 0
1 0 | 1
1 1 | Q=Q’=0
No change
Reset
Set
Invalid
S R | Q
0 0 | Q=Q’=1
0 1 | 1
1 0 | 0
1 1 | Q0
Invalid
Set
Reset
No change

## Slide 21: SR Latch
S R | Q
0 0 | Q0
0 1 | 0
1 0 | 1
1 1 | Q=Q’=0
No change
Reset
Set
Invalid
S’ R’ | Q
0 0 | Q=Q’=1
0 1 | 1
1 0 | 0
1 1 | Q0
Invalid
Set
Reset
No change

## Slide 22: Controlled Latches
C S R | Q
0 x x | Q0
1 0 0 | Q0
1 0 1 | 0
1 1 0 | 1
1 1 1 | Q=Q’
No change
No change
Reset
Set
Invalid
SR Latch with Control Input

## Slide 23: Controlled Latches
C D | Q
0 x | Q0
1 0 | 0
1 1 | 1
No change
Reset
Set
C
Timing Diagram
D
Q
t
Output may change
D Latch (D = Data)

## Slide 24: Controlled Latches
C D | Q
0 x | Q0
1 0 | 0
1 1 | 1
No change
Reset
Set
C
Timing Diagram
D
Q
Output may change
D Latch (D = Data)

## Slide 25: Graphic symbols for latches

## Slide 26: Level versus edge sensitivity
Since the output of the D latch is controlled by the level (0 or 1) of the clock input, the latch is said to be level sensitive
  All of the latches we have seen have been level sensitive
It is possible to design a storage element for which the output only changes at the point in time when the clock changes from one value to another
  Such circuits are said to be edge triggered

## Slide 27: Flip-Flops
Controlled latches are level-triggered
Flip-Flops are edge-triggered
C
CLK
Positive Edge
CLK
Negative Edge

## Slide 28: Flip-Flops
D Latch
(Master)
D
C
Q
D Latch
(Slave)
D
C
Q
Q
D
CLK
CLK
D
QMaster
QSlave
Looks like it is negative edge-triggered
Master
Slave
Master-Slave D Flip-Flop

## Slide 29: Flip-Flops
The circuit samples the D input and changes its output at the negative edge of the clock, CLK.
When the clock is 0, the output of the inverter is 1. The slave latch is enabled and its output Q is equal to the master output Y. The master latch is disabled (CLK = 0).
When the CLK changes to high, D input is transferred to the master latch. The slave remains disabled as long as CLK is low. Any change in the input changes Y,but not Q.
The output of the flip-flop can change when CLK makes a transition 1 → 0

## Slide 30: Flip-Flops
D
Q
Q
D
Q
Q
Positive Edge
Negative Edge
Edge-Triggered D Flip-Flop

## Slide 31: Flip-Flops: Edge-Triggered D Flip-Flop

## Slide 32: Flip-Flops
Set-up time and hold time are times required before and after the clock transition that data must be present to be reliably clocked into the flip-flop.
Setup time is the minimum time for the data to be present before the clock.
Hold time is the minimum time for the data to remain after the clock.
CLK
D
CLK
D
Set-up time, ts
Hold time, tH

## Slide 33: JK Flip-Flops
JK Flip-Flop : D = JQ’ + K’Q
When J = 1 and K = 0, D = 1 → next clock edge sets output to 1.
When J = 0 and K = 1, D = 0 → next clock edge resets output to 0.
When J = 1 and K = 1, D= Q’ → next clock edge complements output.
When J = 0 and K = 0, D= Q → next clock edge leaves output unchanged.

## Slide 34: JK Flip-Flops
JK Flip-Flop
D = JQ’ + K’Q
J
Q
Q
K

## Slide 35: T Flip-Flops
T Flip-Flop
D = TQ’ + T’Q = T  Q
J
Q
Q
K
T
D
Q
Q
T
D = JQ’ + K’Q
T
Q
Q

## Slide 36: Flip-Flop Characteristic Tables
D
Q
Q
D | Q(t+1)
0 | 0
1 | 1
Reset
Set
J | K | Q(t+1)
0 | 0 | Q(t)
0 | 1 | 0
1 | 0 | 1
1 | 1 | Q’(t)
No change
Reset
Set
Toggle
J
Q
Q
K
T
Q
Q
T | Q(t+1)
0 | Q(t)
1 | Q’(t)
No change
Toggle

## Slide 37: Flip-Flop Characteristic Equations
D
Q
Q
D | Q(t+1)
0 | 0
1 | 1
Q(t+1) = D
J | K | Q(t+1)
0 | 0 | Q(t)
0 | 1 | 0
1 | 0 | 1
1 | 1 | Q’(t)
Q(t+1) = JQ’ + K’Q
J
Q
Q
K
T
Q
Q
T | Q(t+1)
0 | Q(t)
1 | Q’(t)
Q(t+1) = T  Q

## Slide 38: Flip-Flops with Asynchronous/Direct Inputs
Asynchronous Reset
D
Q
Q
R
Reset
R’ | D | CLK | Q(t+1)
0 | x | x | 0
1 | 0 | ↑ | 0
1 | 1 | ↑ | 1

## Slide 39: Flip-Flops with Direct Inputs
Asynchronous Reset

## Slide 40: Flip-Flops with Direct Inputs
Asynchronous Preset and Clear
PR’ | CLR’ | D | CLK | Q(t+1)
1 | 0 | x | x | 0
0 | 1 | x | x | 1
1 | 1 | 0 | ↑ | 0
1 | 1 | 1 | ↑ | 1
D
Q
Q
CLR
Reset
PR
Preset

## Slide 41: Analysis of Clocked Sequential Circuits: The State
State = Values of all Flip-Flops
Example
A B = 0 0

## Slide 42: Analysis of Clocked Sequential Circuits: Terminology
State Equation: A state equation (transition equation) specifies the next state as a function of the present state and inputs.
State Table: A state table (transition table) consists of: present state, input, next state and output.
State Diagram: The information in a state table can be represented graphically in a state diagram. The state is represented by a circle and the transitions between states are indicated by directed lines connecting the circles.

## Slide 43: Analysis of Clocked Sequential Circuits: State/Transition Equations
A(t+1) = DA
= A(t) x(t)+B(t) x(t)
= A x + B x
B(t+1) = DB
= A’(t) x(t)
= A’ x
y(t) = [A(t)+ B(t)] x’(t)
= (A + B) x’

## Slide 44: Analysis of Clocked Sequential Circuits: State /Transition Table
A(t+1) = A x + B x
B(t+1) = A’ x
y(t) = (A + B) x’
Present State |  | Input | Next State |  | Output
A | B | x | A | B | y
0 | 0 | 0 |  |  | 
0 | 0 | 1 |  |  | 
0 | 1 | 0 |  |  | 
0 | 1 | 1 |  |  | 
1 | 0 | 0 |  |  | 
1 | 0 | 1 |  |  | 
1 | 1 | 0 |  |  | 
1 | 1 | 1 |  |  | 
t+1
t
t
0 0 0
0 1 0
0 0 1
1 1 0
0 0 1
1 0 0
0 0 1
1 0 0

## Slide 45: Analysis of Clocked Sequential Circuits: State/Transition Table
A(t+1) = A x + B x
B(t+1) = A’ x
y(t) = (A + B) x’
Present State |  |  | Next State |  |  |  | Output | 
 |  |  | x = 0 |  | x = 1 |  | x = 0 | x = 1
A |  | B | A | B | A | B | y | y
0 |  | 0 | 0 | 0 | 0 | 1 | 0 | 0
0 |  | 1 | 0 | 0 | 1 | 1 | 1 | 0
1 |  | 0 | 0 | 0 | 1 | 0 | 1 | 0
1 |  | 1 | 0 | 0 | 1 | 0 | 1 | 0
t+1
t
t

## Slide 46: Analysis of Clocked Sequential Circuits: State Diagram
0 0
1 0
0 1
1 1
0/0
0/1
1/0
1/0
1/0
1/0
0/1
0/1
AB
input/output
Present State |  |  | Next State |  |  |  | Output | 
 |  |  | x = 0 |  | x = 1 |  | x = 0 | x = 1
A |  | B | A | B | A | B | y | y
0 |  | 0 | 0 | 0 | 0 | 1 | 0 | 0
0 |  | 1 | 0 | 0 | 1 | 1 | 1 | 0
1 |  | 0 | 0 | 0 | 1 | 0 | 1 | 0
1 |  | 1 | 0 | 0 | 1 | 0 | 1 | 0

## Slide 47: Analysis of Clocked Sequential Circuits: D Flip-Flops
Example:
D
Q
Q
x
CLK
y
A
Present State | Input |  | Next State
A | x | y | A
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
1 | 1 | 1 | 
0
1
1
0
1
0
0
1
0
1
00,11
00,11
01,10
01,10
A(t+1) = DA = A  x  y

## Slide 48: Analysis of Clocked Sequential Circuits: JK Flip-Flops
Example:
JA = B KA = B x’
JB = x’ KB = A  x
A(t+1) = JA Q’A + K’A QA
= A’B + AB’ + Ax
B(t+1) = JB Q’B + K’B QB
= B’x’ + ABx + A’Bx’
Present State |  | I/P | Next State |  | Flip-Flop Inputs |  |  | 
A | B | x | A | B | JA | KA | JB | KB
0 | 0 | 0 |  |  |  |  |  | 
0 | 0 | 1 |  |  |  |  |  | 
0 | 1 | 0 |  |  |  |  |  | 
0 | 1 | 1 |  |  |  |  |  | 
1 | 0 | 0 |  |  |  |  |  | 
1 | 0 | 1 |  |  |  |  |  | 
1 | 1 | 0 |  |  |  |  |  | 
1 | 1 | 1 |  |  |  |  |  | 
0 0 1 0
0 0 0 1
1 1 1 0
1 0 0 1
0 0 1 1
0 0 0 0
1 1 1 1
1 0 0 0
0 1
0 0
1 1
1 0
1 1
1 0
0 0
1 1

## Slide 49: Analysis of Clocked Sequential Circuits: JK Flip-Flops
Present State |  | I/P | Next State |  | Flip-Flop Inputs |  |  | 
A | B | x | A | B | JA | KA | JB | KB
0 | 0 | 0 |  |  |  |  |  | 
0 | 0 | 1 |  |  |  |  |  | 
0 | 1 | 0 |  |  |  |  |  | 
0 | 1 | 1 |  |  |  |  |  | 
1 | 0 | 0 |  |  |  |  |  | 
1 | 0 | 1 |  |  |  |  |  | 
1 | 1 | 0 |  |  |  |  |  | 
1 | 1 | 1 |  |  |  |  |  | 
0 0 1 0
0 0 0 1
1 1 1 0
1 0 0 1
0 0 1 1
0 0 0 0
1 1 1 1
1 0 0 0
0 1
0 0
1 1
1 0
1 1
1 0
0 0
1 1
0 0
1 1
0 1
1 0
1
0
1
0
1
0
0
1
Example:

## Slide 50: Analysis of Clocked Sequential Circuits: T Flip-Flops
Example:
TA = B x TB = x
y = A B
A(t+1) = TA Q’A + T’A QA
= AB’ + Ax’ + A’Bx
B(t+1) = TB Q’B + T’B QB
= x  B
Present State |  | I/P | Next State |  | F.F Inputs |  | O/P
A | B | x | A | B | TA | TB | y
0 | 0 | 0 |  |  |  |  | 
0 | 0 | 1 |  |  |  |  | 
0 | 1 | 0 |  |  |  |  | 
0 | 1 | 1 |  |  |  |  | 
1 | 0 | 0 |  |  |  |  | 
1 | 0 | 1 |  |  |  |  | 
1 | 1 | 0 |  |  |  |  | 
1 | 1 | 1 |  |  |  |  | 
0 0
0 1
0 0
1 1
0 0
0 1
0 0
1 1
0 0
0 1
0 1
1 0
1 0
1 1
1 1
0 0
0
0
0
0
0
0
1
1

## Slide 51: Analysis of Clocked Sequential Circuits: T Flip-Flops
Example:
Present State |  | I/P | Next State |  | F.F Inputs |  | O/P
A | B | x | A | B | TA | TB | y
0 | 0 | 0 |  |  |  |  | 
0 | 0 | 1 |  |  |  |  | 
0 | 1 | 0 |  |  |  |  | 
0 | 1 | 1 |  |  |  |  | 
1 | 0 | 0 |  |  |  |  | 
1 | 0 | 1 |  |  |  |  | 
1 | 1 | 0 |  |  |  |  | 
1 | 1 | 1 |  |  |  |  | 
0 0
0 1
0 0
1 1
0 0
0 1
0 0
1 1
0 0
0 1
0 1
1 0
1 0
1 1
1 1
0 0
0
0
0
0
0
0
1
1
0 0/0
0 1/0
1 1/1
1 0/0
0
1
0
1
1
1
0
0

## Slide 52: Mealy and Moore Models
The Mealy model: the outputs are functions of both the present state and inputs
  The outputs may change if the inputs change during the clock pulse period.
The Moore model: the outputs are functions of the present state only
  The outputs are synchronous with the clocks.

## Slide 53: Mealy and Moore Models
Block diagram of Mealy and Moore state machine

## Slide 54: Mealy and Moore Models
Present State |  | I/P | Next State |  | O/P
A | B | x | A | B | y
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0 | 1
0 | 1 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 1
1 | 1 | 1 | 1 | 0 | 0
Mealy
For the same state, the output changes with the input
Present State |  | I/P | Next State |  | O/P
A | B | x | A | B | y
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0
0 | 1 | 0 | 0 | 1 | 0
0 | 1 | 1 | 1 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 1 | 1 | 1
1 | 1 | 1 | 0 | 0 | 1
Moore
For the same state, the output does not change with the input

## Slide 55: Moore State Diagram
State / Output
0 0 / 0
0 1 / 0
1 1 / 1
1 0 / 0
0
1
1
1
0
0
0
1

## Slide 56: State reduction
Sequential circuit analysis
Circuit diagram state table (or state diagram)
Sequential circuit design
State diagram (state table) circuit diagram
Redundant state may exist in a state diagram (or table)
By eliminating them may reduce the # of flip-flops

## Slide 57: State Reduction
  Only the input-output sequences are important.
  Two circuits are equivalent
    Have identical outputs for all input sequences;
    The number of states is not important.
State diagram
State: | a | a | b | c | d | e | f | f | g | f | g | a
Input: | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 
Output: | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 

## Slide 58: State Reduction
Equivalent states
  Two states are said to be equivalent
    For each member of the set of inputs, they give exactly the same output and send the circuit to the same state or to an equivalent state.
  One of them can be removed.

## Slide 59: State Reduction

## Slide 60: State Reduction
Reducing the state table
  e = g (remove g);
  d = f (remove f);

## Slide 61: State Reduction
  The reduced finite state machine
State: | a | a | b | c | d | e | d | d | e | d | e | a
Input: | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 
Output: | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 

## Slide 62: State Reduction: Implication Table
The state-reduction procedure for completely specified state tables is based on the algorithm that two states in a state table can be combined into one if they can be shown to be equivalent.
There are occasions when a pair of states do not have the same next states, but, nonetheless, go to equivalent next states
The checking of each pair of states for possible equivalence in a table with a large number of states can be done systematically by means of an implication table.

## Slide 63: State Reduction: Implication Table
(a, b) imply (c, d) and (c, d) imply (a, b). Both pairs of states are equivalent; i.e., a and b are equivalent as well as c and d.

## Slide 64: State Reduction:Implication Table

## Slide 65: State Reduction: Implication Table
  Finally, all the squares that have no crosses are recorded with check marks. The equivalent states are: (a, b), (d, e), (d, g), (e, g).
  We now combine pairs of states into larger groups of equivalent states. The last three pairs can be combined into a set of three equivalent states (d, e, g) because each one of the states in the group is equivalent to the other two.

## Slide 66: State Reduction: Implication Table
  The final partition of these states consists of the equivalent states found from the implication table, together with all the remaining states in the state table that are not equivalent to any other state: (a, b) (c) (d, e, g) (f)

## Slide 67: Implied Equivalences Extending Over a Number of States
  5 = 6 if 6 = 7, 5 = 7 if 5 = 6, 6 = 7 if 5 =7
  1 = 2 and 5 = 6, 5 = 7, 6 = 7 i.e. 5 = 6 = 7

## Slide 68: Implied Equivalences Extending Over a Number of States
  5 = 6 if 6 = 7, 5 = 7 if 5 = 6, 6 = 7 if 5 =7
  1 = 2 and 5 = 6, 5 = 7, 6 = 7 i.e. 5 = 6 = 7

## Slide 69: Implied Equivalences Extending Over a Number of States
  Alternative definition of equivalence:
  Two circuit states with the same output conditions can be made equivalent, unless the equivalence depends upon a known non- equivalence.

## Slide 70: State Assignment
Assign coded binary values to the states for physical implementation
For a circuit with m states, the codes must contain n bits where 2n >= m
Unused states are treated as don’t care conditions during the design
  Don’t cares can help to obtain a simpler circuit
There are many possible state assignments
  Have large impacts on the final circuit size

## Slide 71: Popular State Assignment

## Slide 72: State Assignment
Any binary number assignment is satisfactory as long as each state is assigned a unique number
Use binary assignment 1

## Slide 73: Design Procedure
Derive a state diagram for the circuit from specifications
Reduce the number of states if necessary
Assign binary values to the states
Obtain the binary-coded state table
Choose the type of flip-flop to be used
Derive the simplified flip-flop input equations and output equations
Draw the logic diagram

## Slide 74: Design of Clocked Sequential Circuits
S0 / 0
S1 / 0
S3 / 1
S2 / 0
0
1
1
0
0
1
0
1
State | A B
S0 | 0 0
S1 | 0 1
S2 | 1 0
S3 | 1 1
Example:
Detect 3 or more consecutive 1’s

## Slide 75: Design of Clocked Sequential Circuits
Present State |  | Input | Next State |  | Output
A | B | x | A | B | y
0 | 0 | 0 |  |  | 
0 | 0 | 1 |  |  | 
0 | 1 | 0 |  |  | 
0 | 1 | 1 |  |  | 
1 | 0 | 0 |  |  | 
1 | 0 | 1 |  |  | 
1 | 1 | 0 |  |  | 
1 | 1 | 1 |  |  | 
0 0 0
0 1 0
0 0 0
1 0 0
0 0 0
1 1 0
0 0 1
1 1 1
S0 / 0
S1 / 0
S3 / 1
S2 / 0
0
1
1
0
0
1
0
1
Example:
Detect 3 or more consecutive 1’s

## Slide 76: Design of Clocked Sequential Circuits
Present State |  | Input | Next State |  | Output
A | B | x | A | B | y
0 | 0 | 0 |  |  | 
0 | 0 | 1 |  |  | 
0 | 1 | 0 |  |  | 
0 | 1 | 1 |  |  | 
1 | 0 | 0 |  |  | 
1 | 0 | 1 |  |  | 
1 | 1 | 0 |  |  | 
1 | 1 | 1 |  |  | 
0 0 0
0 1 0
0 0 0
1 0 0
0 0 0
1 1 0
0 0 1
1 1 1
A(t+1) = DA (A, B, x)
= ∑ (3, 5, 7)
B(t+1) = DB (A, B, x)
= ∑ (1, 5, 7)
y (A, B, x) = ∑ (6, 7)
Synthesis using D Flip-Flops
Example:
Detect 3 or more consecutive 1’s

## Slide 77: Design of Clocked Sequential Circuits with D F.F.
DA (A, B, x) = ∑ (3, 5, 7)
= A x + B x
DB (A, B, x) = ∑ (1, 5, 7)
= A x + B’ x
y (A, B, x) = ∑ (6, 7)
= A B
Synthesis using D Flip-Flops
 |  |  |  | B | 
 |  | 0 | 0 | 1 | 0
A |  | 0 | 1 | 1 | 0
 |  |  | x |  | 
 |  |  |  | B | 
 |  | 0 | 1 | 0 | 0
A |  | 0 | 1 | 1 | 0
 |  |  | x |  | 
 |  |  |  | B | 
 |  | 0 | 0 | 0 | 0
A |  | 0 | 0 | 1 | 1
 |  |  | x |  | 
Example:
Detect 3 or more consecutive 1’s

## Slide 78: Design of Clocked Sequential Circuits with D F.F.
DA = A x + B x
DB = A x + B’ x
y = A B
Synthesis using D Flip-Flops
Example:
Detect 3 or more consecutive 1’s

## Slide 79: Flip-Flop Excitation Tables
Present State | Next State | F.F. Input
Q(t) | Q(t+1) | D
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
Present State | Next State | F.F. Input | 
Q(t) | Q(t+1) | J | K
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
0 0 (No change)
0 1 (Reset)
0 x
1 x
x 1
x 0
0
1
0
1
1 0 (Set)
1 1 (Toggle)
0 1 (Reset)
1 1 (Toggle)
0 0 (No change)
1 0 (Set)
Q(t) | Q(t+1) | T
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
0
1
1
0

## Slide 80: Design of Clocked Sequential Circuits with JK F.F.
Present State |  | Input | Next State |  | Flip-Flop Inputs |  |  | 
A | B | x | A | B | JA | KA | JB | KB
0 | 0 | 0 | 0 | 0 |  |  |  | 
0 | 0 | 1 | 0 | 1 |  |  |  | 
0 | 1 | 0 | 0 | 0 |  |  |  | 
0 | 1 | 1 | 1 | 0 |  |  |  | 
1 | 0 | 0 | 0 | 0 |  |  |  | 
1 | 0 | 1 | 1 | 1 |  |  |  | 
1 | 1 | 0 | 0 | 0 |  |  |  | 
1 | 1 | 1 | 1 | 1 |  |  |  | 
0 x
0 x
0 x
1 x
x 1
x 0
x 1
x 0
JA (A, B, x) = ∑ (3)
dJA (A, B, x) = ∑ (4,5,6,7)
KA (A, B, x) = ∑ (4, 6)
dKA (A, B, x) = ∑ (0,1,2,3)
JB (A, B, x) = ∑ (1, 5)
dJB (A, B, x) = ∑ (2,3,6,7)
KB (A, B, x) = ∑ (2, 3, 6)
dKB (A, B, x) = ∑ (0,1,4,5)
Synthesis using JK F.F.
0 x
1 x
x 1
x 1
0 x
1 x
x 1
x 0
Example:
Detect 3 or more consecutive 1’s

## Slide 81: Design of Clocked Sequential Circuits with JK F.F.
Example:
Detect 3 or more consecutive 1’s
JA = B x KA = x’
JB = x KB = A’ + x’
Synthesis using JK Flip-Flops
 |  |  |  | B | 
 |  | 0 | 0 | 1 | 0
A |  | x | x | x | x
 |  |  | x |  | 
 |  |  |  | B | 
 |  | x | x | x | x
A |  | 1 | 0 | 0 | 1
 |  |  | x |  | 
 |  |  |  | B | 
 |  | 0 | 1 | x | x
A |  | 0 | 1 | x | x
 |  |  | x |  | 
 |  |  |  | B | 
 |  | x | x | 1 | 1
A |  | x | x | 0 | 1
 |  |  | x |  | 

## Slide 82: Design of Clocked Sequential Circuits with T F.F.
Example:
Detect 3 or more consecutive 1’s
Present State |  | Input | Next State |  | F.F. Input
A | B | x | A | B | TA TB
0 | 0 | 0 | 0 | 0 | 
0 | 0 | 1 | 0 | 1 | 
0 | 1 | 0 | 0 | 0 | 
0 | 1 | 1 | 1 | 0 | 
1 | 0 | 0 | 0 | 0 | 
1 | 0 | 1 | 1 | 1 | 
1 | 1 | 0 | 0 | 0 | 
1 | 1 | 1 | 1 | 1 | 
0
0
0
1
1
0
1
0
Synthesis using T Flip-Flops
0
1
1
1
0
1
1
0
TA (A, B, x) = ∑ (3, 4, 6)
TB (A, B, x) = ∑ (1, 2, 3, 5, 6)

## Slide 83: Design of Clocked Sequential Circuits with T F.F.
Example:
Detect 3 or more consecutive 1’s
TA = A x’ + A’ B x
TB = A’ B + B  x
Synthesis using T Flip-Flops
 |  |  |  | B | 
 |  | 0 | 0 | 1 | 0
A |  | 1 | 0 | 0 | 1
 |  |  | x |  | 
 |  |  |  | B | 
 |  | 0 | 1 | 1 | 1
A |  | 0 | 1 | 0 | 1
 |  |  | x |  | 

## Slide 84: Design of Clocked Sequential Circuits with T F.F.
Example:
3-bit binary counter

## Slide 85: Design of Clocked Sequential Circuits with T F.F.

## Slide 86: Design of Clocked Sequential Circuits with D F.F.
Design a one-input, one-output serial 2's complementer. The circuit accepts a string of bits from the input and generates the 2's complement at the output. The circuit can be reset asynchronously to start and end the operation.

## Slide 87: Design of Clocked Sequential Circuits with D F.F.

## Slide 88: Design of Clocked Sequential Circuits with D F.F.

## Slide 89: Syllabus
Chapter 5 (Excluding Section 5.6)